## Slide 1: Photo-cathode RF Gun: Cathode and Vacuum
Mostafa Salahshoor
22 Sep 2020
School of Particles and Accelerators - IPM
In the name of Allah

## Slide 2: Content
Introduction
    Linac – Injector – Gun
    Electron Emission and Extraction Mechanisms
    Thermionic DC Gun vs. Photocathode RF Gun
Photocathode
    Three Step Model – Quantum Efficiency
    Classification – Properties
  Vacuum
    Describing Vacuum – Flow Regimes – Need for Accelerators
    Sources of gas loads – Outgassing
    Cathode Preparation, Transport & Characterization Systems

## Slide 3: IPM Linac Layout
Injector

## Slide 4: Injectors
Emission & Initial Acceleration
Thermionic cathode
Gridded-DC gun
DC gun
NCRF gun
Photo-electric cathode
DC gun
NCRF gun
SRF gun
Field-emission cathode
Pulsed-DC
RF
Pulsed-DC+
NCRF
Beam Conditioning
Emittance compensation
Solenoid focusing
RF focusing
Slice phase space matching
Ballistic compression
Fundamental & sub-harmonic RF
Inductive linac
Magnetic compression
RF harmonic linearizing
RF compression
Solenoid focusing
Tapered RF phase bunching
Acceleration
Capture into booster
Emittance preservation
Longitudinal phase space compensation
Chirping for bunch compressors
Gun

## Slide 5: Electron Gun in Accelerators
Electron source or electron gun is a device which provides electrons for accelerators.
It essentially needs:
  an electron generation mechanism
  and an extraction mechanism.
Extraction
Generation

## Slide 6: Electron Generation Mechanism
Give the conduction band electrons extra energy
  Thermionic Emission
  Photoelectric Emission (Photochathode)
  Secondary Emission
Change the potential barrier
  Field Emission or “tunneling”
  Plasma Emission

## Slide 7: Emission Mechanisms
Thermal Emission
Richardson-Dushman
Field Emission
Fowler Nordheim
Photo Emission
Fowler-Dubridge

## Slide 8: Thermionic and Field Emitters
Good for true DC and long pulse duration applications
The good points:
  Simple
  Low transverse emittance
  Tolerant of poor vacuum
  Long lifetime
However:
  Long bunches (100 ps+)
  Large longitudinal emittance
  Lack of control of profile
  Complicate Linac (Bunchers, Compressors)

## Slide 9: Why use a Photo-Injector?
High peak current density ( 10^5 A/cm^2 )
Low emittance/temperature ( <0.2 μm‐rad )
Electron beam properties determined by laser
  Timing and repetition rate
  Spatial Profile
  Bunch length and temporal profile (Sub‐ps bunches are possible)

## Slide 10: Electron Extraction Mechanism
DC RF

## Slide 11: Thermionic DC Gun vs. Photocathode RF Gun
 | Thermionic DC Gun | Photocathode RF Gun
Type of emission | DC | Pulse
Current | High average current possible | High peak current possible
Post Buncher | Mandatory | Not needed
Output energy | few tens of KeV | MeV
Emittance per nC | ~ 10 -12 π-mm-mrad | <2 π-mm-mrad
Main usage | High current industrial, medical | Research accelerators

## Slide 12: Photocathode RF Gun
ELYSE

## Slide 13: Section II
Photocathode
    Three Step Model – Quantum Efficiency
    Classification – Properties

## Slide 14: QE of Photocathodes
The efficiency of a photocathode is measured by its quantum efficiency :
@ 266 nm

## Slide 15: Three-step model
Energy
Medium
Vacuum
Φ
Vacuum level
Filled States
Empty States
h
Excitation of e- in metal
  Reflection (angle dependence)
  Energy distribution of excited e-
2) Transit to the Surface
e--e- scattering
Direction of travel
3) Escape surface
Overcome Work function
Reduction of  due to applied
  field (Schottky Effect)
Laser
Integrate product of probabilities over all electron energies capable of escape to obtain Quantum Efficiency
?

## Slide 16: Schottky Effect
Under the RF field, the surface barrier of the emissive material is deformed to be lower. The generated electrons can be liberated to the vacuum more easily.

## Slide 17: QE vs thermal emittance
QE and emittance have the same dependency on photon energy.
We can reduce emittance at the expense of very low QE.

## Slide 18: Factors Affecting QE
Factor | Description
Reflection | Choice of polarization and angle of incidence Light traps (microstructures)
Nonproductive absorption | Semiconductor cathodes (especially NEA materials) Narrow valence band Work function reduction (Schottky effect, dipole layers)
Electron scattering (electron mfp) | Stay within the “magic window”, f<Eg<2Egap Minimize photon absorption length (surface plasmons) Good crystals – minimize defect and impurity
Deposition parameters | Substrate material, cathode thickness, sequential vs Co-deposition, substrate temperature, cooling time, oxide layer formation
Vacuum environment | Ion back-bombardment, electron stimulated desorption, chemical poisoning
Operating environment | Thermal stability, space charge

## Slide 19: Factors Affecting Dark Current
Low work function reduces the threshold photon energy and improves QE, especially near threshold,
But, it increases dark current.
=> Optimal work function depends on application.
Mechanism | Factors
Field emission | Electric field at cathode Surface morphology Work function
Thermal emission | Temperature Work Function
Ion bombardment | Vacuum Work function

## Slide 20: Cathodes for electron guns

## Slide 21: Positive Electron Affinity (PEA) Negative Electron Affinity (NEA)
NEA
PEA
Electron affinity = the energy released when an electron is attached to a neutral atom

## Slide 22: The Old Standby - Metals
Response Time: time required for excited electrons to escape
Lifetime: time required for QE to drop to 1/e of initial

## Slide 23: Superconducting Photocathodes

## Slide 24: Properties of metal cathodes
Metal Cathodes | Wavelength & Energy: λopt (nm), ℏω (eV) | Quantum Efficiency (electrons per photon) | Vacuum for 1000h operation (Torr) | Work Function, φw (eV) | Thermal Emittance (microns / mm(rms)) Eq. (1) | Thermal Emittance (microns / mm(rms)) Expt.
Bare Metal |  |  |  |  |  | 
Cu | 250, 4.96 | 1.4 x 10-4 | 10-9 | 4.6 [2] | 0.5 | 1.0 ± 0.1 [3]
 |  |  |  |  |  | 1.2 ± 0.2 [4]
 |  |  |  |  |  | 0.9 ± 0.05 [5]
Mg | 266, 4.66 | 6.4 x 10-4 | 10-10 | 3.6 [6] | 0.8 | 0.4 ± 0.1 [6]
Pb | 250 , 4.96 | 6.9 x 10-4 | 10-9 | 4.0 [2] | 0.8 | ?
Nb | 250 , 4.96 | ~2 x 10-5 | 10-10 | 4.38 [2] | 0.6 | ?
Coated Metal |  |  |  |  |  | 
CsBr:Cu | 250 , 4.96 | 7 x 10-3 | 10-9 | ~2.5 | ? | ?
CsBr:Nb | 250 , 4.96 | 7 x 10-3 | 10-9 | ~2.5 | ? | ?

## Slide 25: Semiconductor Photocathodes

## Slide 26: Properties of semiconductor cathodes (PEA)
Cathode Type | Cathode | Typical Wavelength & Energy, λopt (nm), (eV) | Quantum Efficiency (electrons per photon) | Vacuum for 1000 h (Torr) | Gap Energy + Electron Affinity, EG+EA (eV) | Thermal Emittance (microns / mm(rms)) Eq. (2) | Thermal Emittance (microns / mm(rms)) Expt.
PEA: mono-alkali | Cs2Te | 211, 5.88 | 0.1 | 10-9 | 3.5 [7] | 1.2 | 0.5 ± 0.1 [8]
 |  | 262, 4.70 | - | - | " | 0.9 | 0.7 ± 0.1 [8]
 |  | 262, 4.73 | - | - | " | 0.9 | 1.2 ± 0.1 [9]
 | Cs3Sb | 432, 2.87 | 0.15 | ? | 1.6 + 0.45 [7] | 0.7 | ?
 | K3Sb | 400, 3.10 | 0.07 | ? | 1.1 + 1.6 [7] | 0.5 | ?
 | Na3 | 330, 3.76 | 0.02 | ? | 1.1 + 1.6 [7] | 0.4 | ?
 | Li3Sb | 295, 4.20 | 0.0001 | ? | ? | ? | ?
PEA: multi-alkali | Na2KSb | 330, 3.76 | 0.1 | 10-10 | 1 + 1 [7] | 1.1 | ?
 | (Cs)Na3KSb | 390, 3.18 | 0.2 | 10-10 | 1 + 0.55 [7] | 1.5 | ?
 | K2CsSb | 543, 2.28 | 0.1 | 10-10 | 1+1.1 [7] | 0.4 | ?
 |  | 532 |  |  |  |  | 0.56 ± 0.03 [10]
 | K2CsSb(O) | 543, 2.28 | 0.1 | 10-10 | 1 + <1.1 [7] | ~0.4 | ?

## Slide 27: Properties of semiconductor cathodes (NEA)
Cathode Type | Cathode | Typical Wavelength & Energy, λopt (nm), (eV) | Quantum Efficiency (electrons per photon) | Vacuum for 1000 h (Torr) | Gap Energy + Electron Affinity, EG+EA (eV) | Thermal Emittance (microns / mm(rms)) Eq. (2) | Thermal Emittance (microns / mm(rms)) Expt.
NEA | GaAs(Cs,F) | 532, 2.33 | 0.1 | ? | 1.4 ± 0.1 [7] | 0.8 | 0.44 ± 0.01 [11]
 |  | 860, 1.44 | 0.1 | ? |  | 0.2 | 0.22 ± 0.01 [11]
 | GaN(Cs) | 260, 4.77 | 0.1 | ? | 1.96 + ? [11] | 1.35 | 1.35 ± 0.1 [12]
 | GaAs(1-x)Px x~0.45 (Cs,F) | 532, 2.33 | 0.1 | ? | 1.96 + ? [11] | 0.49 | 0.44 ± 0.1 [11]
S-1 | Ag-O-Cs | 900, 1.38 | 0.01 | ? | 0.7 [7] | 0.7 | ?

## Slide 28: Summary of Cathodes Properties
Metal Cathodes
Good response time (<<1ps)
Very robust and insensitive to vacuum
Very low QE (<0.01%)
Need UV light
PEA Cathodes
Work in visible light
High QE (>1%)
Good response time (<1ps)
Need very good vacuum (~10-10 torr or better)
NEA Cathodes
Work in visible light
High QE (>10%)
Possible to attain sub-thermal mean transverse energies
Need very good vacuum (~10-12 torr or better)
Response time very long (~100ps) in IR/red wavelengths, but less than 1ps in green

## Slide 29: Section III
Vacuum
    Describing Vacuum – Flow Regimes – Need for Accelerators
    Sources of gas loads – Outgassing
    Cathode Preparation, Transport & Characterization Systems

## Slide 30: Vacuum
 | Pa | kg/cm2 | Torr | mbar | bar | atm
1 Pa | 1 | 10.2 10-6 | 7.5 10-3 | 10-2 | 10-5 | 9.81 10-6
1 kg/cm2 | 98.1 103 | 1 | 735.5 | 980 | 0.98 | 0.96
1 Torr | 133 | 1.35 10-3 | 1 | 1.33 | 1.33 10-3 | 1.31 10-3
1 mbar | 101 | 1.02 10-3 | 0.75 | 1 | 10-3 | 0.98 10-3
1 bar | 1.01 105 | 1.02 | 750 | 103 | 1 | 0.98
1 atm | 101 300 | 1.03 | 760 | 1 013 | 1.01 | 1
= sub-atmospheric pressure.
The force exerted on the walls of an evacuated vessel surrounded by atmospheric pressure is: 1 kg/cm2

## Slide 31: Describing Vacuum

## Slide 32: Flow Regimes
Re > 2000 | turbulent
Re < 1000 | viscous

## Slide 33: Why do we need vacuum in particle accelerator?
Less beam-gas interaction:
  Increase beam lifetime,
  Prevents to increase beam size,
  Reduces radiation hazard,
  Lowers background in detectors.
The total beam lifetime in a particle accelerator is given by:
Not only the absolute pressure is important but also what are the gas species in the system

## Slide 34: Sources of gas loads
Generic vacuum system
Sources of static gas loads
in vacuum system:

## Slide 35: What process defines the pressure over time?

## Slide 36: Thermal Outgassing

## Slide 37: Outgassing Rates

## Slide 38: Dynamic Outgassing

## Slide 39: Photon Stimulated Desorption

## Slide 40: Photon Stimulated Desorption

## Slide 41: Vacuum Systems
Vacuum Pumps (molecular regime)
  Momentum transfer pumps
    Turbo Molecular Pump
  Capture pumps (getters)
    evaporable getters (Titanium Sublimation Pump - TSP)
    non-evaporable getters - NEG (Sputter ion pumps)
Vacuum Gauges
Vacuum Valves
Other Vacuum Components (Flange, Gasket, …)

## Slide 42: Vacuum Requirements Related to Photocathode RF Gun
Cathode Preparation System
Cathode Manipulation and Installation System
Cathode Transport System
Cathode Characterization System
Cathode Performance and Life Time
RF Breakdown
Semiconductor and
coated metal cathodes

## Slide 43: Cs2Te Cathodes production and use

## Slide 44: Cathodes production and use: substratum

## Slide 45: Cathodes production and use: evaporation

## Slide 46: Cathodes production and use: growth

## Slide 47: Cathodes production and use: gun operation

## Slide 48: Photocathodes Studies @ FLASH
Photocathode inserted into the gun backplane

## Slide 49: Photocathode Production: Preparation Chamber
Photocathodes are grown @ LASA on Mo plugs under UHV condition.

## Slide 50: Production: from Mo plugs ...

## Slide 51: Production: ... to photocathodes growth

## Slide 52: Characterization: diagnostic on photocathodes

## Slide 53: Transport: from LASA to FLASH and PITZ

## Slide 54: CW QE measurements: Experimental set-up

## Slide 55: Standard evaporation process

## Slide 56: Co-evaporation process

## Slide 57: SwissFEL LOAD-LOCK SYSTEM

## Slide 58: Preparation chamber
where cathodes can be cleaned, annealed and where the quantum efficiency (QE) can be checked.

## Slide 59: Vacuum suitcase
where cathode plugs can be loaded from preparation chamber and transported to the gun.

## Slide 60: Gun loading chamber
which is permanently attached to the gun and in which cathodes can be transferred from vacuum suitcase to the gun backplane.

## Slide 61: SwissFEL LOAD-LOCK SYSTEM

## Slide 62: Preparation System – Instrumentation Requirements
QE measurement system
laser + chopper wheel + lock-in amp + photodetector - Used to shine light of known power on the cathode. The Lockin-amp +chopper not required if background light is negligible.
Current measurement - Electrons emitted from the cathode can be collected in a electrode placed close to the cathode surface at a certain bias (~100V). Alternatively, if the sample is floated, the electron current emitted can also be measured by recording the current flowing into the sample. The ammeter should be capable of reading currents from pA range to the uA range.
Quartz Micro Balance (QMB)
Used to estimate the mass of the material deposited. Ideally this should be placed in a position which sees the same flux of material as the substrate.

## Slide 63: Preparation System - Instrumentation Requirements
Vacuum Monitoring
RGA - Records the partial pressures of various residual gases in the chamber
Cold cathode gauge /Ion gauge - Records the total pressure in the prep chamber
Thermocouple + heater - Used to control temperature of the substrate.

## Slide 64: Survivability and Lifetime: Cathode Contamination
Three sources of cathode contamination
Residual contaminants left by fabrication, handling and storage
Contamination and damage by the RF gun and laser
  Ambient vacuum
  Operating vacuum
  Cathode cleaning
Contamination during operation due to molecular cracking:
  By the laser
  By the electron beam
Toward problem solution
Cathode exchange (last choice)
Cathode restoration
  Laser Cleaning
  Surface sputtering
  UV/Ozone Cleaning (from the beamline experience)

## Slide 65
Thank You